## Slide 1: PhysioNet Challenge – AF classification
Speaker: Yu-Cheng, Lin
Advisor:
Date: 2019/10/03

## Slide 2: Outline
Paper survey(14,17,20)
Discussion
Reference

## Slide 3
Paper 14

## Slide 4: About this paper
Title: Can Supervised Learning Be Used to Classify Cardiac Rhythms?
Author: Marcus Vollmer, Philipp Sodmann, Leonard Caanitz, Neetika Nath, Lars Kaderali
Final accuracy: 0.81

## Slide 5: Framework
Training CNN model for generating annotation sequence
Feature extraction
Random forest classifier

## Slide 6: Annotation sequence
Mapping ECG signal to annotation sequence(R,P,T,~,O,unknown)
R, P, T from QT-database [1], O from MIT-BIT database [2]
~ by realistic noise generate by WFDB
Refer to [1]
Refer to [2]

## Slide 7: Training CNN model
Database: QT database & MIT-BIH arrhythmia database & generated noisy signal
Augmentation: 17ms window size, add white noise
Training data: Total 12,000,000 charateristic waveform
Result: 99.7% accuracy for 50ms tolerance

## Slide 8: Feature extraction
Absolute value, interquatiles range for RR, RT, PR intervals
Percentage of extrasystoles(single, doublets, triplets)
Silhoutte score(compute correlation of each pair of heart beat +> kmeans on the basis of correlation metrics )

## Slide 9: Training
Random forest classfier

## Slide 10
Paper 17

## Slide 11: About this paper
Title: Rhythm and Quality Classification from Short ECGs Recorded Using a Mobile Device
Author: Joachim A. Behar, Aviv A. Rosenberg, Yael Yaniv, Julien Oster
Final accuracy: 0.80

## Slide 12: Framework
Preprocessing
Feature extraction
SVM classifier

## Slide 13: Preprocessing
Use jqrs to detect R-peaks
Jqrs/epltd/ggrs detectors were used to estimate the quality of the signal by bsqi

## Slide 14: Feature extraction
Signal quality
Predictability of RR intervals
ECG morphology(QRS duration, QT interval, …)
Heart rate variability
Fragmentation measures

## Slide 15: Training result
Cascaded classification due to unbalanced data
First: N/OA~
Second: A/O~
Third: ~/O

## Slide 16: Training result
Top five features for distinguishing
N/OA~: minrr, AVNN, PAS, medR, medST
A/O~: IrE, CosEn, AFE, F1, medianrr
~/O: medTamp, PACe, stdP, F1, stdR

## Slide 17
Paper 20

## Slide 18: About this paper
Title: Hierarchical Cardiac-Rhythm Classification Based on Electrocardiogram Morphology
Author: Dionisije Sopic, Elisabetta De Giovanni, Amir Aminifar, David Atienza
Final accuracy: 0.80

## Slide 19: Framework

## Slide 20: Preprocessing
Bandpass filter 0.05~40(Hz)
R-peaks are detected using Pan-Tompkins algorithm

## Slide 21: Feature extraction
HR-based features: statistical features of
P/T-wave features: statistical features, Shannon entropy, normalized power of concatenate P/T-waves
Time & frequency domain features: QT/QRS-width & normalized signal power at [0.05,50] and [50,fs/2] in order to detect noise ?
Additional features: zero-crossing of P/T-waves

## Slide 22: Training & Results
Normalize all features
Multiclass Classifiation(ECOC) Boosting(100 weak learners)
Random forest classifier(binary classify O/N) Boosting(400 weak learners)
?

## Slide 23: Discussion
P2 - Centerwave features
P8 - Log-spectrogram
P8 - Augmentation(Dropout-burst, Random resampling)
How to find out noisy signal?
How to choose expert features?

## Slide 24: Reference
[1] A Database for Evaluation of Algorithms for Measurement of QT and Other Waveform Intervals in the ECG, P Laguna, RG Mark, A Goldberg, GB Moody,
[2] The impact of the MIT-BIH Arrthythmia Database, George B. Moody, Roger G. Mark