## Slide 1: PhysioNet Challenge – AF classification
Speaker: Yu-Cheng, Lin
Advisor:
Date: 2019/10/14

## Slide 2: Outline
Analysis, Observation and solutions of the whole data
Analysis, Observation and solutions of each class of data
About QRS detector

## Slide 3: Analysis of the whole data
Length distribution of all data
Amount of data of each class
Length distribution of each class

## Slide 4: Observation and solutions
Extreme data unbalancing
  How it affect F1-score?
  How to train it?
Large amount of signals are of length ~10000
  How to padding?
  Maybe all to 10000 and cut long data into half
Length distribution of noisy signal is much more different
  Detect noisy data first

## Slide 5: Analysis of signals of each class

## Slide 6
noisy
Flip up&down
Higher peak
Up?down?
Normal

## Slide 7
AF

## Slide 8
Other

## Slide 9
Noisy

## Slide 10: Observation and solutions
N/A/O:
  Some unusual pulse(usually at front): detect and remove it
  Some noisy signals: detect(maybe by correlation) and remove it
  Uneven average-R-peaks: normalize it
  Signals upside down: flip it back but how to detect?
~:
  Difficult to detect R-peaks
  Often has unusual pulse

## Slide 11: About QRS detector
Using WFDB package
XQRS detection(detect upside down ?)
XQRS detect of inverted signal is not the same
About XQRS algorithm / PAN-Tompkins algorithm

## Slide 12: About QRS detector(Pan-Tompkins algorithm)
BP-filter(cascade by LP&HP filter in original proposal) 5~15 Hz with some specific transfer function in order to reduce muscle noise, powerline interference …
Derivative filter with specific transfer function to get the slope of QRS
Square
Moving average

## Slide 13: About QRS detector(Pan-Tompkins algorithm)
Fiducial mark: the signal changes direction (from an increasing direction to a decreasing direction)
Thresholds
  Each fiducial mark is considered as a potential QRS
  At the beginning of the QRS detection, a 2 seconds learning phase is needed to initialize SignalLevelI and NoiseLevelI as a percentage of the maximum and average amplitude of the integrated signal, respectively.
  The threshold is automatically updated after detecting a new peak, based on its classification as signal or noise peak
  the algorithm implements a further check before confirming the peak as a true QRS, taking into consideration the information provided by the bandpass filtered signal.
Search back for missed QRS complexes
T wave discrimination
  The algorithm takes particularly into consideration the possibility of a false detection of T waves.

## Slide 14: Observation
About 10% inverted signal
Distribution in ‘x’ is dependent to ‘noisy’
How to detect if a signal is inverted?
  Threshold of the ratio of +/-
Others
Others

## Slide 15: Discussion
Expanded data:
  Random cutting signal
  Some noisy signal maybe windowed
Short data:
  Need to remove noisy & unusual signal
Raw data:
  Some Noisy signal
  Unusual pulse
Center wave data:
  Maybe choose more center wave
QRS data:

## Slide 16: Future work
Preprocessing – remove noisy & unusual signal
Solve reversal lead problem
Implement center wave data algorithm